## Slide 1: Satellite Navigation using GNSS

## Slide 2: Outline
Basics of Satellite Navigation
  GNSS Systems
  GPS System, Measurements, Performance
Augmentation Systems
  Differential GPS (DGPS)
  Space Based Augmentation Systems (SBAS)
  Ground Based Augmentation Systems (GBAS)
Practical Applications
Scientific Exploration
  Ionospheric Studies
  Space Weather
Summary

## Slide 3: GNSS Systems Compatible and Interoperable
Galileo (EU)
Beidou/COMPASS (China)
GLONASS
Global Positioning System (GPS)

## Slide 4: The Global Positioning System (GPS)
Worldwide Radio-Navigation System
  Developed and maintained by U.S. DoD
  Original intended use was military
  Early-on civilian use was enabled
Provide 3D Positioning, Velocity and Time
  24hrs/day,7 days/wk, everywhere!
GPS Consists of Three Segments
  Space Segment
  Control Segment
  User Segment
Based on Satellite Ranging
  Users determine position by measuring the
GPS Space Segment
distance from a group of satellites in space

## Slide 5: The Global Positioning System (GPS)
GPS Control Segment
Original intended use was military
Early-on civilian use was enabled
Provide 3D Positioning, Velocity and Time
  24hrs/day,7 days/wk, everywhere!
GPS Consists of Three Segments
  Space Segment
  Control Segment
  User Segment
Based on Satellite Ranging
  Users determine position by measuring the distance from a group of satellites in space
Worldwide Radio-Navigation System
  Developed and maintained by U.S. DoD
User Segment:
You and 200 Million other people

## Slide 6: The Global Positioning System (GPS)
6 Monitor Stations
1 Master Control Station 3 Ground Antennas
Worldwide Radio-Navigation System
  Developed and maintained by U.S. DoD
  Original intended use was military
  Early-on civilian use was enabled
Provide 3D Positioning, Velocity and Time
  24hrs/day,7 days/wk, everywhere!
GPS Consists of Three Segments
  Space Segment
  Control Segment
  User Segment
Based on Satellite Ranging
Users determine position by measuring the distance from a group of satellites in space

## Slide 7: How does it work? Trilateration by Satellite
First measurement puts us somewhere on
this sphere.
Measurement from a second satellite shows we are somewhere on this circle where the first and
second spheres interrsect
Third measurement from another satellite places us at one of two points.
A fourth measurement will give us time!

## Slide 8: Sources of GPS Errors
Receiver clock errors
Signal multipath
Orbital errors
Number of satellites visible
Satellite geometry
Tropospheric and Ionospheric delays
(www.garmin.com)
Typical Standard Positioning Service (SPS) GPS position accuracy:
~10-15 meters (mostly due to the ionosphere)
Good DOP
Poor HDOP
Poor VDOP

## Slide 9: Two Levels of GPS Service
Precise Positioning Service (PPS)
  Authorized users ONLY
  U. S. and Allied military
  Requires cryptographic equipment, specially equipped receivers
  Accurate to 21 meters 95% of time
Standard Positioning Service (SPS)
  Available to all users
  Accuracy degraded by Selective Availability until May 2000
    Horizontal accuracies ~100 m
  Current accuracy similar to PPS (≤15m)
    Less for Augmented GPS: DGPS,SBAS,GBAS

## Slide 10: GPS Augmentations
Why augment?
  For better accuracy: Mitigate measurement errors
  For robustness: Mitigate effects of
    RFI (intentional or not)
    Signal attenuation due to blockage (foliage, building, or temporary loss of signal
How augment?
  Transmit corrections for errors that are correlated spatially and temporally
    Differential GPS
    Wide Area Differential GPS
      Space Based Augmentation Systems (SBAS)
    Local Area Augmentation Systems (GBAS)
  Assist GPS receiver with complementary technologies (e.g. intertial), signals of opportunity (eLoran), or offloading some functions (to a cell tower in E911)
Based on P. Misra, 2009

## Slide 11: Differential GPS (DGPS)
Uses 2 receivers
  Reference receiver
  Remote/roving receiver
Reference receiver calculates the errors in the received GPS signals
Transmits corrections to rover receiver
  via radio link or mobile phone
Public and private reference beacon stations are available
  US Nationwide NDGPS
  US Maritime MDGPS
  40 other countries have similar systems
DGPS Accuracy: ~1–3 m Degrades with distance

## Slide 12: Real Time Kinematic
BASE STATION OVER KNOWN POINT
ROVER
Centimeter Accuracy
10
Figure from Dorota Brzezinska

## Slide 13: Satellite Based Augmentation Systems (SBAS) Designed to improve GPS accuracy, availability and integrity for civil aviation.
Courtesy of the FAA
Future primary means of civil air navigation
For all aircraft in all phases of flight
  Non-Precision Approach (NPA) – en-route
Vertically Guided Approach (LPV) – runway
First of many worldwide systems – EGNOS, MSAS, GAGAN
Current Infrastructure:
38 Reference Stations
3 Master Stations
4 Uplink stations
2 Communications Satellites
WAAS message provides:
  corrections for satellite orbits,
time and the ionosphere
  estimates of the uncertainty of
those corrections
WAAS Accuracy: ~1–3 m

## Slide 14: Satellite Based Augmentation Systems (SBAS) (ICAO is committed to transition to satellite navigation)
WAAS
EGNOS
GAGAN
MSAS
CSTB
WAAS operational in 2003
EGNOS – The European Satellite Augmentation System – 2009
MSAS – The Asia Pacific Satellite Augmentation System – 2007
CSTB – South American Satellite Augmentation System - TBD
GAGAN – Indian Satellite Augmentation System – TBD
SNAS – Chinese Satellite Navigation Augmentation System - TBD
Systems in equatorial regions will face more
challenging ionospheric dynamics.
CWAAS
SNAS

## Slide 15: Ground Based Augmentation System (GBAS)
Provides local airport coverage:
~20-30 mile radius
4 Receivers; 1 VHF radio data link from a ground-based transmitter
Precision Approach for CAT- I, II, III
Procedures for Arrival and Departure
Multiple runway coverage at an airport terminal area
Demonstrated accuracy is < 1 meter
LAAS
Local Area Augmentation System

## Slide 16: LAAS/GBAS International Efforts
n.
en
Rio De Janeiro, Brazil
Agana, Guam
Malaga, Spain
Sydney, Australia
Frankfurt, Germany
Bremen, Germany

## Slide 17: Typical GPS Ranging Errors
Error Source | SPS GPS | Differential GPS | RTK
User Range Errors |  |  | 
System Errors Ephemeris Data Satellite Clocks | 0.4 -0.5 m 1-1.2m | Removed Removed | Removed Removed
Atmospheric Errors Ionosphere Troposphere | 0.5 – 5m 0.2 -0.7m | 0.2 – 2.0m Removed | 0.0005 - .01m Removed
Total Typical URE Errors | 1.7 – 7.0m | 0.2 – 2.0m | 0.0005-0.01m
User Equipment Errors |  |  | 
Receiver | 0.1 – 3m | 0.1 – 3m | Almost All Removed
Multipath | 0-10m | 0-10m | Greatly Reduced

## Slide 18: Applications
Annual Commerce in GPS Products and Services > $10billion
>200 Million Users

## Slide 19: Precision Approach & Landing (SBAS&GBAS) Improves the accuracy, integrity and availability of GNSS
Efficiency
  More direct en-route paths
  Greater runway availability
  Precision Approach for all users
Cost
  Low cost avionics
  Reduction of ground based navigation
aides
Safety
  Vertical Guidance for all phases of flight
    takeoff, en-route to precision approach
  Available at all runway poor visibility
  Situational Awareness
FAA
GARMIN Aircraft Receiver

## Slide 20: Detroit, Mich., 3 Dec. 1990 Northwest Airlines DC-9
DC9, lost in fog, blunders onto an active runway and is struck by departing 727. 8 dead, 22 injured

## Slide 21: Exxon Valdez, March 24, 1989 Ran Aground on Bligh’s Reef
2008, Institute of Navigation, Per Enge

## Slide 22: Exxon Valdez (continued)
2008, Institute of Navigation, Per Enge
10.8 Million Gallons of Oil Spilled

## Slide 23: Smart Phones
Smart Phones (cell phone + PDA)
  GPS used for emergency calls
  Emergency location
  Applications include:
  Basic maps
  Turn by turn directions
  $200 – $400
Cell Phones with GPS embedded
  Mostly for E911 calls only

## Slide 24: Scientific Exploration with GNSS
Seismic monitoring & prediction
Volcano monitoring
Climate change
Gravity fields
Atmospheric science
  ground water vapor
  the ionosphere
  space weather

## Slide 25: Ionospheric Effects on GPS
TEC
  Induces Range Errors
  Highly variable with location, time, season, magnetic and solar activity
Scintillation
  Induces rapid changes in amplitude and phase of incoming signal
  Can induce cycle slips and loss of lock that degrade performance

## Slide 26: The LISN Network using >75 GPS Receivers

## Slide 27: GNSS for Scientific Research in Africa
Africa has a most challenging
ionosphere :
Strong latitudinal gradients
Within northern and southern anomaly peaks
Covers a wide longitudinal region
Depletions and scintillation are potentially the worst conditions worldwide
The Worldwide Ionosphere

## Slide 28: Ionospheric Monitors in Africa
13 units of MAGDAS
7 units of GPS including SCINDA,
4 units of AWESOME
20 units of SID monitors
data obtained from these facilities are being used to improve our understanding of space weather as it affects the performance of GNSS
Additional monitors:
3 units GPS from BC –
More planned under ICTP/BC partnership
Ionosondes planned
Based on presentation by Dr. Rabiu Babatunde

## Slide 29: Solar Cycle Dependence all effects intensify with increasing solar activity

## Slide 30: Simple Summary
GNSS is an enabling technology that can make major contributions to economic growth and societal betterment. It is also a key to scientific exploration.

## Slide 31: Thanks !